## Slide 1
The application of the BrilLanCe series scintillation
detector in the spectrometer of neutral particles for
the satellite experiment ZINA-NT
Arkhangelskaja I.V., Arkhangelsky A.I., Batischev, A.G., Galper A.M., Kondratyeva N.V., Naumov P. Yu.
National Nuclear University “MEPhI”

## Slide 2
Studying of GRB X-ray and -emission included HE up to 300 MeV
Detailed investigation of GRB spectra in wide energy band
Space weather monitoring
Magnetospheric particles flows monitoring
Studying flows of charged particles and n during solar flares
Investigation of X-ray and -emission during solar flares (including 15.11 MeV and 20.58 MeV lines)
Investigation of X-ray and -emission of TGF
THE EXPERIMENT GOALS & TASKS

## Slide 3
Multilayer scintillator detector (МSD) – NRNU “MEPhI”, Russia;
Detector of neutral particle (DNP) – NRNU “MEPhI”, Russia;
Processor System – Physics Institute of NAS of Belorussia.
ZINA-NT experiment detectors
MSD detector
DNP detector

## Slide 4
Energy bands:
Electrons and positrons 4 - 25 MeV
Protons and He nuclei 40 - 110 MeV/nucleon
Energy resolution:
Protons and He nuclei 1,5 - 4%
Electrons 6 - 8%
geometric quotient 40 cm2*sr
aperture 80 o
Time resolution 100 ns
Parameters of МSD

## Slide 5
C 12 – 3
top view
front view
TRIGGER: МSТ=(АС) × С11,
АС=(С14 OR С13 OR С12-1 OR С12-2 OR С12-3 OR С12-4)
Back current timing analysis t (C11-AC)>0.5ns
(if fast scintillator used)
scintillator
crystal
scintillator
crystal
PMT
PMT
PMT
PMT
PMT
PMT
PMT
polystyrene
The function diagram of ZINA-NT detector
C 11

## Slide 6
Scintillator class BrilLanCe – used firstly in Delft University (Netherland)
Produced by: SAINT GOBAIN CERAMICS & PLASTICS
BrilLanCe350
LaCl3:Ce (10%Сe)
BrilLanCe380
LaBr3:Ce (5%Сe)

## Slide 7
Characteristics | NaI(Tl) | CsI(Tl) | LaBr3:Ce | LaCl3:Ce
Light output , quanta/кeV | 38 | 45 | 65 | 48
Fast time (tf), ns | 220 | 700 | 18 | 25
Slow time (ts), ms | 1,4 | 2-5 | 0,8 unstable | 0,5
Relation between components(C1\C2) at 25оС, % | 85:15 | 50:450 | 90:10 | 80:20
fluorescence from HE charged particles | weakly | Up to 20 ms | weakly | weakly
Density, g/sм3 | 3,67 | 4,51 | 5,08 | 3,85
λ, nm ( at light maximum) | 410 | 565 | 380 | 350
Mechanical stress res. | low | high | high | high
Energy resolution (662 кeV) | 7% | 9% | 2,9% | 3,8%
Water resistance | yes | no | weakly | weakly (at high To)
Radiation hardness, rad | 105 | 107 | 1,5x107 | 107
Main characteristics of NaI(Tl), CsI(Tl) & BrilLanCe crystals
( all has at least two lightoutput components)

## Slide 8
The temperature dependence of relative pulse height
relative pulse height

## Slide 9
Pulse shape in CsI(Tl) crystal

## Slide 10
Pulse shape in LaBr3:Ce crystal
The slow component is unstable- identification on base of fast component

## Slide 11
Pulse shape in NaI(Tl) crystal
very strong temperature dependence!

## Slide 12
Pulse shape in LaCl3:Ce crystal

## Slide 13
A some light components in scintillators | 
CsI(Tl) t1~0.4-0.7s t2~7s | A particle with different ionizing capability can be sorting by the pulse shape analyzing method
LaCl3:Ce t1~25 ns t2~0,5s | 
LaBr3:Ce t1~20 ns t2~0,8s (unstable) | 

## Slide 14
The ratio Qslow/Qtot in dependence of energy in CsI(Tl)

## Slide 15
The fast and slow light component temperature dependence for the LaCl3:Ce crystal

## Slide 16
Relative light intensity (fast and slow component) vs temperature for scintillator LaCl3:Ce

## Slide 17
ADC channel
ADC channel
137Cs  5.4%
(662 keV)
137Am  20%
(59,5 keV)
3”x 3” crystal + PMT EMI9265-B53/FL

## Slide 18
22Na  6%
(511 keV)
133Ba  16%
(87 кeV)
133Ba  7%
(356 кeV)
ADC channel
ADC channel
3”x3” crystal + PMT EMI9265-B53/FL

## Slide 20
wide region of linearity of BrilLanCe series crystals!

## Slide 21
3 possible opportunities of DNP
in ZINA-NT experiment
6’ x 6’ CsI(Tl)
  energy band 100 keV-300MeV (-quanta)
  min time resolution ~ 1 ms
  problem with high intensity events
6’’ x 6’’ NaI(Tl)-CsI(Tl)
  energy band 50 keV-300MeV (-quanta)
  min time resolution ~ 1 ms
  reduced fluorescence from HE charged particles
  min time resolution ~ 1 ms
  problem with high intensity events
6’’ x 6’’ BrilLanCe350 (LaCl3:Ce (10%Сe))

## Slide 22
negative
positive
CONCLUSIONS: BrilLanCe series crystal in DNP instead of CsI(Tl):
energy resolution is better ( the factor of 2-3 )
low limit of detector energy band ~20 keV instead of 100 keV;
temperature stability is better;
lightoutput components are faster (the factor of the order) :
 time resolution: ~5 s (instead of 1ms) for  up to 20 MeV,
~15s(instead of 10ms)for events need analysis of pulse shape(HE and n);
 several parallel timescales: s (instead of ms),1s,10s,64s and 128s for events with low statistic (15.11 and 20.58 MeV nuclear lines in solar flares,
GRB extended emission and so on);
 registration of more intensive fluxes;
 possibility of remove ~90% of back current!!
pulse shape discrimination require additional analysis;
self radioactivity caused by 0.09% of 138La and mixture of 27Ac;
very fast ADC and special electronics.

## Slide 23
ZINA-NT will be installed
onboard ISS at 2015
Now this project is open for collaboration!
Special thanks to prof. W.Q. Gan from PMO (China) for very useful discussion

## Slide 24: Thank you for attention!